## Slide 1: Rechargeable Battery Degradation Prediction and Classification
Tai-Jung Chen
05/03

## Slide 2: Outlines
Background
Data Description
Data Preprocessing
Modeling
Results
Acknowledgement

## Slide 3: Background

## Slide 4: Background
Lithium-ion batteries are widely used in nowadays
When will the battery die out?
Knowing the State of Health (SOH) would help allocate the battery system properly
Aiming on using early life cycles to predict SOH
Data-driven Machine learning algorithm are often used
In this project:
MIT dataset
Gradient Boosting Regression Tree (GBRT)
Extreme Gradient Boosting (XGBoost)
Notes: Phone battery
Car inspection

## Slide 5: Data Description

## Slide 6: Data Description
Photo credit:
< X. Song et al.: Combined CNN-LSTM Network for SOC Estimation of Lithium-Ion Batteries >
The dataset consists of 124 commercial lithium-ion batteries cycled to failure under fast-charging conditions
These lithium-ion phosphate (LFP)/graphite cells, manufactured by A123 Systems (APR18650M1A)
Failure = cycle to 80% of nominal capacity (0.88 Ah)
Cycled in the 48-channel Arbin LBT potentiostat
Temperature chamber set to 30°C

## Slide 7: Data Description
0%
80%
100%
72 different policy
1C-3.6V
4C-2.0V
< Fast charge policy >
<SOC>

## Slide 8: Data Description
< Look for one particular cell for example >

## Slide 9: Data Preprocessing

## Slide 10: Data preprocessing
Raw Data
One Batch
43
<2018/4/12>
Two Batches
46
<2018/4/12 + 2017/6/30>
Three Batches
42
<2018/4/12 + 2017/6/30 +2017/5/12>
43 cells
89 cells
Accumulated cells
131 cells

## Slide 11
Remove cycle life >= 1600
Before
After
131 examples
126 examples

## Slide 12: Data preprocessing
Data Frame
Number Of Cells = 126
Number of Features = 72
< F. Yang et al. “Lifespan prediction of lithium-ion batteries based on various extracted features and gradient boosting regression tree model” >

## Slide 13: Data preprocessing
< IC curve of two particular cells >

## Slide 14: Data preprocessing
Var() is highly correlated to the cycle life.
Notes: discharge capacity is Q

## Slide 15: Data preprocessing
Model A is a Linear regression model.
Model B and C semi-empirical models and have been widely used to capture the capacity degradation of lithium-ion batteries.

## Slide 16: Data preprocessing
Constructed by Temperature data during discharge process.
Discharge time (min)
Discharge time (min)

## Slide 17: Data preprocessing
Data Frame
Number Of Cells = 126
Number of Features = 72

## Slide 18: Modeling

## Slide 19: Modeling
Gradient Boosting Regression Tree
< Slide credit: StatQuest with Josh Starmer >
Take Learning rate, number of trees, and number of splits as the hyper parameters

## Slide 20: Modeling
Extreme Gradient Boosting (XGBoost)
< Slide credit: StatQuest with Josh Starmer >
,
Take Learning rate, number of trees, number of splits, lambda, and gamma as the hyper parameters

## Slide 21: Modeling
Training and Validation Set
Evaluation Set
2/3
Number of Features = 72
1/3
<Data Frame>
Training Set
Validation Set
4/5
1/5
Number of Features = 72
5-fold cross validation

## Slide 22: Modeling
<Learning Rate>
<Number of trees>
<Maximum Number of Split>
Go over 5-fold CV on all the combinations
Return a list of
Pick the best hyper parameter based on RMSE
<gamma>
<lambda>

## Slide 23: Modeling
<Learning Rate>
<Number of trees>
<Maximum Number of Split>
Go over 5-fold CV on all the combinations
Return a list of
Pick the best hyper parameter based on RMSE
<gamma>
<lambda>
epoch: perform different training and evaluation set

## Slide 24: Results

## Slide 25: Result
Adding lambda and gamma
Top 4 epochs with fixed hyper param on XGBoost | RMSE | MAE | MAPE | R^2 | R^2 adj
lr = 0.05; num_tree=500; max_split=1; lmb=1; gamma = 96 | 82.2472 | 57.3341 | 8.37% | 0.8577 | 0.6644
 | 77.1562 | 58.1224 | 7.12% | 0.8921 | 0.7455
 | 77.9134 | 59.2571 | 9.15% | 0.8795 | 0.7157
 | 68.8885 | 55.9075 | 7.97% | 0.8845 | 0.7277
mean | 76.5513 | 57.6553 | 0.081549 | 0.87845 | 0.71333
std | 5.57922 | 1.40735 | 0.008462 | 0.01477 | 0.03484

## Slide 26: Result
Adding only lambda
top 4 epochs with fixed hyper param on XGBoost | RMSE | MAE | MAPE | R^2 | R^2 adj
lr = 0.05; num_tree=500; max_split=1; lmb=1 | 83.7588 | 64.5968 | 8.90% | 0.8802 | 0.7175
 | 83.3241 | 63.5248 | 9.27% | 0.8604 | 0.6708
 | 80.1853 | 62.0573 | 8.59% | 0.8594 | 0.6684
 | 83.025 | 65.9253 | 8.10% | 0.8755 | 0.7064
mean | 82.5733 | 64.0261 | 0.0871643 | 0.86888 | 0.69078
std | 1.62026 | 1.63912 | 0.0049796 | 0.01055 | 0.02489

## Slide 27: Comparison
MIT dataset paper:
on training set; on validation set; on evaluation set
Chen and Yang:
5-fold cross validation
on training and validation set; on evaluation set (random split)
 | Model | Hyper-parameter tuning | RMSE
MIT | Linear Regression | Full model | 100
Yang | GBRT | Learning rate; number of trees; maximum split | 84.91
Chen | XGBoost | Learning rate; number of trees; maximum split; Lambda | 82.57
Chen | XGBoost | Learning rate; number of trees; maximum split; Lambda; Gamma | 76.55

## Slide 28: Result
Using XGBoost to classify battery lifespan thresholding on 550 cycle
best_lr: 0.2, best_num_tree: 100, best_max_split: 1 | Accuracy | Precision | Recall | F1 score
 | 97.62 % |  |  | 
0 (short lifespan) |  | 0.92 | 1 | 0.96
1 (long lifespan) |  | 1 | 0.97 | 0.98
 | 95.24 % |  |  | 
0 (short lifespan) |  | 1 | 0.88 | 0.93
1 (long lifespan) |  | 0.93 | 1 | 0.96

## Slide 29: Acknowledgement
Thanks to Prof. Kwok Tsui for advising.
Thanks to Dr. Fangfang Yang for providing details and answering questions from paper.

## Slide 30
Thank You! Q&A

## Slide 31: Data Description
< Look for one particular cell for example >

## Slide 32
Features for the MIT dataset

## Slide 33: Modeling
<Learning Rate>
<Number of trees>
<Maximum Number of Split>
Go over 5-fold CV on all the combinations
Return a list of
Pick the best hyper parameter based on RMSE
epoch: perform different training and evaluation set

## Slide 34: Results- run 20 epochs
 | RMSE | MAE | MAPE (%) | R^2 | R^2 adj
best_lr: 0.25, best_num_tree: 900, best_max_split: 8 | 113.41 | 88.23 | 13.53 | 0.7661 | 0.4483
best_lr: 0.2, best_num_tree: 700, best_max_split: 1 | 119.21 | 96.17 | 12.37 | 0.7355 | 0.3762
best_lr: 0.15, best_num_tree: 300, best_max_split: 4 | 100.01 | 77.61 | 10.64 | 0.8292 | 0.5972
best_lr: 0.2, best_num_tree: 800, best_max_split: 32 | 98.03 | 75.26 | 10.49 | 0.8208 | 0.5774
best_lr: 0.5, best_num_tree: 1000, best_max_split: 8 | 114.65 | 83.25 | 11.62 | 0.7158 | 0.3297
best_lr: 0.1, best_num_tree: 600, best_max_split: 4 | 88.81 | 70.99 | 10.17 | 0.836 | 0.6132
best_lr: 0.25, best_num_tree: 1000, best_max_split: 32 | 84.96 | 61.33 | 8.02 | 0.8781 | 0.7125
best_lr: 0.05, best_num_tree: 500, best_max_split: 4 | 104.40 | 81.81 | 10.63 | 0.8085 | 0.5483
best_lr: 0.25, best_num_tree: 700, best_max_split: 8 | 96.35 | 73.23 | 9.49 | 0.8496 | 0.6453
best_lr: 0.15, best_num_tree: 900, best_max_split: 4 | 114.19 | 89.24 | 13.44 | 0.7567 | 0.4262
best_lr: 0.01, best_num_tree: 1000, best_max_split: 1 | 116.05 | 90.87 | 12.65 | 0.7708 | 0.4594
best_lr: 0.2, best_num_tree: 100, best_max_split: 2 | 122.24 | 92.52 | 14.33 | 0.7363 | 0.3781
best_lr: 0.15, best_num_tree: 500, best_max_split: 4 | 107.16 | 77.11 | 11.53 | 0.7857 | 0.4946
best_lr: 0.05, best_num_tree: 400, best_max_split: 2 | 95.55 | 68.28 | 9.96 | 0.8483 | 0.6422
best_lr: 0.15, best_num_tree: 100, best_max_split: 4 | 100.24 | 76.54 | 9.58 | 0.8096 | 0.5509
best_lr: 0.01, best_num_tree: 600, best_max_split: 2 | 91.26 | 69.02 | 8.59 | 0.8552 | 0.6585
best_lr: 0.5, best_num_tree: 800, best_max_split: 1 | 136.90 | 98.75 | 11.11 | 0.759 | 0.4316
best_lr: 0.05, best_num_tree: 300, best_max_split: 1 | 80.14 | 59.23 | 7.29 | 0.8846 | 0.7278
best_lr: 0.5, best_num_tree: 900, best_max_split: 32 | 113.99 | 87.18 | 11.86 | 0.775 | 0.4693
best_lr: 0.25, best_num_tree: 600, best_max_split: 4 | 125.27 | 97.37 | 11.81 | 0.7664 | 0.4491
Mean | 106.14 | 80.70 | 10.96 | 0.7994 | 0.5268
Std | 14.67 | 11.73 | 1.85 | 0.0496 | 0.1169
UL (Mean + 3*Std) | 150.15 | 115.88 | 16.51 | 0.9480 | 0.8774
LL (Mean - 3*Std) | 62.13 | 45.52 | 5.40 | 0.6507 | 0.1762

## Slide 35: Comparison
MIT dataset paper:
on training set; on validation set; on evaluation set
 | RMSE | MAE | MAPE (%) | R^2 | R^2 adj
case 1 | 80.14 | 59.23 | 7.29 | 0.8846 | 0.7278
case 2 | 84.96 | 61.33 | 8.02 | 0.8781 | 0.7125
case 3 | 88.81 | 70.99 | 10.17 | 0.836 | 0.6132
case 4 | 91.26 | 69.02 | 8.59 | 0.8552 | 0.6585
Tai-Jung:
5-fold cross validation
on training and validation set; on evaluation set (random split)
Non-fixed hyper parameter and run 20 epochs

## Slide 36: Future Outlook

## Slide 37: Future Outlook
Feature selection aspects:
  Deep learning-based stacked denoising autoencoder
  Look up the Feature importance and construct better features
Modeling aspects:
  Try other Algorithms such as XGBoost, and Neural Network
Other aspects:
  Data bias and variances between different batches
  Look into the classification problem